Name: Anirban Das Batch: BCSE-II Session: 2020-21
Roll No.: 001910501077
Second Semester Experiments in Microprocessor Lab

Problem Sheet #1

1. Load the contents of the memory locations 2200H and 2201H into registers. Add these registers and store the result in memory locations 2202H and 2203H.

Line#	Address in Hex	Label	Instruction	Opcode (in hex)	Remarks
1	0800		LDA 2200H	3A	A = M[2200H]
2	0801			00
3	0802			22
4	0803		MOV H, A	67	H = A
5	0804		LDA 2201H	3A	A = M[2201H]
6	0805			01
7	0806			22
8	0807		MOV L, A	84	L = A
9	0808		MVI A, 00H	6F	A = 00H
10	0809			3E
11	080A		ADC A	00	A = A + Cy
12	080B			8F
13	080C		MOV H,A	67	H = A
14	080D		SHLD 2202H	22	M[2202H] = L / M[2203H] = H
15	080E			02
16	080F			22
17	0810		HLT	76	Halt

Simulator with loaded machine code:

Sample input and output (M[2200H] = FFH, M[2201H] = F0H; ABH + CDH = 01EFH)

2. Find the sum of N numbers stored in consecutive locations starting from 2500H. The value of N is stored in 2200H. Store the result in locations 2300H and 2301H.

Line#	Address in Hex	Label	Instruction	Opcode in Hex	Remarks
03	0800		LXI H, 2200H	21	Store value of N
	0801			00
	0802			22
04	0803		MOV C, M	4E	C = M
06	0804		LXI H, 2500H	21	Store starting address
	0805			00
	0806			25
07	0807		XRA A	AF	Clear Accumulator
08	0808		MOV E,A	5F	E = A
10	0809	LOOP:	ADD M	86	These 3 steps add to E; preserving flags
11	080A		JNC SKIP	D2	SKIP => Cy = 0
	080B			0E
	080C			00
12	080D		INR E	1C	If carry generated, increment E (higher byte)
14	080E	SKIP:	DCR C	0D	Decrement counter
15	080F		INX H	23	Go to next input
16	0810		JNZ LOOP	C2	Loop back to add if numbers left
	0811			C9
	0812			00
18	0813		LXI H, 2300H	21	Load H with address 2300H
	0814			00
	0815			23
99	0816		MOV M, A	77	M = A
20	0817		INX H	23	Go to next input
21	0818		MOV M, E	73	M = E
23	0819		HLT	76	Halt

Simulator with loaded machine code:

Sample input and output (M[2200H] = 05H, M[2500H] = 01H, M[2501H] = 02H, M[2502H] = 05H, M[2503H] = 04H, M[2504H] = 03H; M[2300H] = 0FH)

3. Find the sum of the least significant 4 bits and most significant 4 bits of a byte stored in memory location 2500H. Store the result in 2550H.

Line#	Address in Hex	Label	Instruction	Opcode in Hex	Remarks
1	0800		LDA 2500H	3A	Get input
2	0801			00
3	0802			25
4	0803		MOV B,A	47	Save input because we need it twice
5	0804		ANI 0FH	E6	Get lower significant 4 bits
6	0805			0F
7	0806		MOV D,A	57	D = lower significant 4 bits
8	0807		MOV A,B	78	Get input number again
9	0808		ANI F0H	E6	Get higher significant 4 bits
10	0809			F0
11	080A		RLC	07	Shift LEFT 4 times to bring them down to lower signficant position for addition
12	080B		RLC	07
13	080C		RLC	07
14	080D		RLC	07
15	080E		ADD D	82	Perform required addition
16	080F		STA 2550H	32	Store to required target address
17	0810			50
18	0811			25
19	0812		HLT	76	Halt

Simulator with loaded machine code:

Sample input and output (M[2500H] = B7H, M[2550H] = 12H):

4. Write a program to count the ‘1’s and ‘0’s of a byte stored in 2500H. Store the result in 2610H and 2511H, respectively.

Line#	Address in Hex	Label	Instruction	Opcode in Hex	Remarks
1	0800		LDA 2500H	3A	Get the input
2	0801			00
3	0802			25
4	0803		MVI D, 00H	16	This is the counter of 0s
5	0804			00
6	0805		MVI C, 08H	0E	This is the counter of total number of bits
7	0806			08
8	0807	LOOP:	RRC	0F	Right Shift the bits by 1
9	0808		JC SKIP	DA	Jump to SKIP IF Cy = 1
	0809			0C
	080A			00
10	080B		INR D	14	If current bit is 0, D++
11	080C	SKIP:	DCR C	0D	1 bit checked, decrement C
12	080D		JNZ COUNT	C2	Keep counting if not all bits have been checked
13	080E			07
14	080F			00
15	0801		MOV A,D	7A	Move the no. Of 0s to D
16	0802		STA 2511H	32	Store the number of 0s
17	0803			11
18	0804			25
19	0805		MVI A, 08H	3E	A = 08H
20	0806		SUB D	92	Get the no. Of 1s
21	0807		STA 2611H	32	Store the no. Of 1s
	0808			10
	0809			26
22	081A		HLT	76	Halt

Simulator with loaded machine code:

Sample input and output (M[2500H] = B7H; M[2510H] = 02H, M[2610H] = 06H):

5. Write a program to sum two 16-bits binary numbers.

We will assume the 16-bit numbers are in 2200 and 2202H respectively, in little-endian order (lower significant byte first). We will store a 16-bit result in 2204H in the same manner.

Line#	Address in Hex	Label	Instruction	Opcode in Hex	Remarks
1	0800		LHLD 2200H	2A	Get first number
2	0801			00
3	0802			22
4	0803		XCHG	EB	Swap DE and HL; we need DE = HL
5	0804		LHLD 2202H	2A	Get second number
6	0805			02
7	0806			22
8	0807		DAD D	19	Add
9	0808		SHLD 2204H	22	Store to target address
10	0809			04
11	080A			22
	080B		MVI A, 00H	3E	A = 00H
	080C			00
	080D		ADC A	8F	A = A + Cy
	080E		STA 2206	32	Store the carry at address 2206H
	080F			06
	0810			22
12	0811		HLT	76	Halt

Simulator with loaded machine code:

Sample input and output ( M[2200H , 2201H] = F0F0H, M[2202H , 2203H] = 0FF0H; M[2504H , 2505H] = FFE0H, M[2506H] = 01H ):