Name: Anirban Das Batch: BCSE-II Session: 2020-21
Roll No.: 001910501077
Second Semester Experiments in Microprocessor Lab

Problem Sheet #2

1. Two numbers MN H and KL H are stored in 2050 H and 2051 H , respectively. Write a program to assemble them as NK H and LM H store them in 2052 H and 2053 H .

Line#	Address in Hex	Label	Instruction	Opcode (in hex)	Remarks
1	0800		LDA 2200H	3A	A = M[2050H]
2	0801			50
3	0802			20
4	0803		MOV B, A	47	B = A
5	0804		ANI 0FH	E6	A = A AND 0FH
6	0805			0F
8	0807		RLC	07	Shift LEFT 4 times to bring them down to lower signficant position for addition
	0808		RLC	07
	0809		RLC	07
	080A		RLC	07
9	080B		MOV C,A	4F	C = A
11	080C		MOV A,B	78	A = B
13	080D		ANI F0H	E6	A = A AND F0H
	080E			F0
14	080F		RLC	07	Shift LEFT 4 times to bring them down to lower signficant position for addition
	0810		RLC	07
	0811		RLC	07
	0812		RLC	07
17	0813		MOV D,A	57	Halt
18	0814		LDA 2051H	3A	A = M[2050H]
	0815			51
	0816			20
21	0817		MOV B,A	47	B = A
22	0818		ANI 0FH	E6	A = A AND 0FH
	0819			0F
24	081A		RLC	07	Shift LEFT 4 times to bring them down to lower signficant position for addition
	081B		RLC	07
	081C		RLC	07
	081D		RLC	07
25	081E		MOV E,A	5F	E = A
26	081F		MOV A,B	78	A = B
27	0820		ANI F0H	E6	A = A AND F0H
	0821			F0
29	0822		RLC	07	Shift LEFT 4 times to bring them down to lower signficant position for addition
	0823		RLC	07
	0824		RLC	07
	0825		RLC	07
33	0826		MOV H,A	47	B = A
34	0827		MOV A,C	79	A = C
35	0828		ADD H	84	A = A + H
36	0829		STA 2052H	32	Store to required target address
	082A			52
	082B			20
39	082C		MOV A,D	7A	A = D
40	082D		ADD E	83	A = A + E
41	082E		STA 2053H	32	Store to required target address
	082F			53
	0830			20
44	0831		HLT	76	Halt

Simulator with loaded machine code:

Sample input and output (M[2050] = F4H, M[2051] = E1H => M[2052] = 4EH, M[2053] = 1FH):

2. Two numbers A & B are stored in 2050 H and 2051 H , respectively. Write a program to perform A×B and store the result in 2052 H and 2053 H .

Line#	Address in Hex	Label	Instruction	Opcode in Hex	Remarks
01	0800		LHLD 2050H	2A	H = M[2050H] L = M[2051H]
02	0801			50
03	0802			20
04	0803		XCGH	EB	D = H & E = L
05	0804		MOV C,D	4A	C = D
06	0805		MVI D,00H	16	D = 00H
	0806			00
08	0807		LXI H, 0000H	21	H = 00H & L = 00H
	0808			00
	0809			00
11	080A	LOOP:	DAD D	19	HL = HL + DE
12	080B		DCR C	0D	C = C-1
13	080C		JNZ LOOP	C2	Repeat the process until C becomes 0.
	080D			0A
	080E			08
16	080F	SKIP:	SHLD 2052H	22	Store at required address.
	0810			52
	0811			20
19	0812		HLT	76	Halt

Simulator with loaded machine code:

Sample input and output (M[2050] = E3, M[2051] = 4F => M[2052] = 0D, M[2053] = 46):

3. N numbers are stored in consecutive m/m location starting from 2050 H . The value N is stored in 204F H .

a) Find the maximum and minimum among the N numbers.

Line#	Address in Hex	Label	Instruction	Opcode in Hex	Remarks
1	0800		LXI H, 204FH	21	Get value of N
2	0801			4F
3	0802			20
4	0803		MOV D,M	56	D = M
5	0804		LXI H, 2050H	21	Get address of first list element
6	0805			50
	0806			20
8	0807		MOV B,M	46	Initialize Max register
9	0808		MOV C,M	4E	Initialize Min register
10	0809	MAX	MOV A,M	7E	Get higher significant 4 bits
11	080A		CMP B	B8	A - B
12	080B		JC MIN	DA	Jump to MIN if Cy = 1
	080C			0F
	080D			08
15	080E		MOV B,A	47	Store current value as if MAX if no carry.
16	080F	MIN	CMP C	B9	A - C
17	0810		JNC SKIP	D2	Jump to SKIP if element is smaller than Accumulator (Cy=0) .
	0811			14
	0812			08
20	0813		MOV C,A	4F	Else store element as MIN
21	0814	SKIP	INX H	23	Go to next address
22	0815		DCR D	15	Decrement N
23	0816		JNZ MAX	C2	Continue the process until N=0
	0817			09
	0818			08
26	0819		LXI H,2200H	21	Load the required address
	081A			00
	081B			22
29	081C		MOV M,B	70	M = max of list = B
30	081D		MOV A,C	79	A = min of list = C
31	081E		STA 2202H	32	Store at required address
	081F			02
	0820			22
34	0821		HLT	76	Halt

Simulator with loaded machine code:

Sample input and output (M[204F] = 05H, M[2050] = 01H, M[2051] = 15H, M[2052] = 05H, M[2053] = 36H, M[2054] = F0H => M[2200] = F0H, M[2202] = 01H):

b) Sort the N numbers in ascending and descending order.

Line#	Address in Hex	Label	Instruction	Opcode in Hex	Remarks
1	0800	START	MVI D, 00H	16	D = 00H
2	0801			00
3	0802		LXI H,	21	D = M
	0803			4F
	0804			20
6	0805		MOV B,M	46	Store count from the list.
7	0806		DCR B	05	D = D - 1
8	0807		INX H	23	Go to next address
9	0808	PREVIOUS	MOV A,M	7E	A = M
10	0809		INX H	23	Go to next address
11	080A		CMP M	BE	A = A - M
12	080B		JC NEXT / / JNC NEXT	DA / D2	Jump TO NEXT if Cy=1 -> ASCENDING / OR / Jump to NEXT if Cy = 0 -> DESCENDING
	080C			14
	080D			08
15	080E		MOV C,M	4E	C = M
16	080F		MOV M,A	77	M = A
17	0810		DCX H	2B	Go to previous address
18	0811		MOV M,C	71	M = C
19	0812		INX H	23	Go to next address.
20	0813		INR D	14	D = D + 1
21	0814	NEXT	DCR B	05	B = B – 1 //one iteration
22	0815		JNZ PREVIOUS	C2	Repeat if B is not 0.
	0816			08
	0817			08
25	0818		MOV A,D	7A	A = D
26	0818		CPI 00H	FE	See if a swap has occured
	081A			00
28	081B		JNZ START	C2	If swap has occured, then repeat from START
	081C			00
	081D			08
31	081E		HLT	76	Halt

Simulator with loaded machine code:

Sample input and output (M[204F] = 05H, M[2050] = 01H, M[2051] = 05H, M[2052] = 04H, M[2053] = 03H, M[2054] = 06H => M[2050] = 01H, M[2051] = 03H, M[2052] = 04H, M[2053] = 05H, M[2054] = 06H & M[2050] = 06H, M[2051] = 05H, M[2052] = 04H, M[2053] = 03H, M[2054] = 01H):

ASCENDING ORDER:

DESCENDING ORDER:

4. N numbers are stored in consecutive m/m location starting from 2050 H . The value N is stored in 204F H . Write a program to copy the even and odd numbers starting from 2100 H and 2200 H , respectively. Store the total no. of even and odd numbers in 2300 H and 2201 H respectively.

Line#	Address in Hex	Label	Instruction	Opcode in Hex	Remarks
1	0800		LDA 204FH	3A	Get the input N.
2	0801			4F
3	0802			20
4	0803		MOV C,A	4F	C = A
5	0804		MVI B, 00H	06	B = 0
6	0805			00
7	0806		LXI H, 2050H	21	Load the starting address of list
	0807			50
	0808			20
10	0809		LXI D, 2100H	11	Load the address to store even numbers
	080A			00
	080B			21
13	080C		DCR C	0D	C = C - 1
14	080D	START1	MOV A,M	7E	A = M
15	080E		ANI 01H	E6	A = A AND 01H / IF A = 0, element is even
	080F			01
17	0810		JZ EVEN	CA	Jump to EVEN if A = 0
18	0811			17
19	0812			08
20	0813		MOV A,M	7E	A = M
21	0814		STAX D	12	Store A in register pair D
22	0815		INX D	13	Go to next address
23	0816		INR B	04	B = B + 1
24	0817	EVEN	INX H	23	Go to next address
25	0818		DCR C	0D	C = C - 1
26	0819		JNZ START1	C2	If C is not 0, repeat
	081A			0D
	081B			08
29	081C		LDA 204FH	3A	Get the input N.
	081D			4F
	081E			20
30	081F		MOV C,A	4F	C = A
31	0820		LXI H, 2050H	21	Load the starting address of list
	0821			50
	0822			20
34	0823		LXI D, 2200H	11	Load the address to store even numbers
	0824			00
	0825			22
37	0826		DCR C	0D	C = C - 1
38	0827	START2	MOV A,M	7E	A = M
39	0828		ANI 01H	E6	A = A AND 01H / IF A = 1, element is even
	0829			01
42	082A		JNZ ODD	C2	Jump to ODD if A = 1
	082B			2C
	082C			08
45	082D		MOV A,M	7E	A = M
46	082E		STAX D	12	Store A in register pair D
47	082F		INX D	13	Go to next address
48	0830	ODD	INX H	23	Go to next address in list
49	0831		DCR C	0D	C = C - 1
50	0832		JNZ START2	C2	If C is not 0, repeat
	0833			27
	0834			08
53	0835		MOV A,B	78	A = B //ccount of even numbes
54	0836		STA 2301H	32	Store the count at required address.
	0837			01
	0838			23
57	0839		LDA 204FH	3A	Load the original N
	083A			4F
	083B			20
60	083C		SUB B	90	A = A - B
61	083D		STA 2300H	32	Store the count at required address.
	083E			00
	083F			23
64	0840		HLT	76	Halt

Simulator with loaded machine code:

Sample input and output (M[204F] = 05H, M[2050] = 01H, M[2051] = 02H, M[2052] = 03H, M[2053] = 04H, M[2054] = 05H => M[2200] = 01H, M[2201] = 03H, M[2202] = 05H, M[2100] = 02H, M[2101] = 04H, M[2300] = 02H, M[2301] = 03H):

ODD NUMBERS:

EVEN NUMBERS:

EVEN AND ODD COUNT:

5. N numbers are stored in consecutive m/m location starting from 2050 H . The value N is stored in 204F H . Write a program to test whether a number stored in 204E H is present in the list. If present, store its position in the list at 204D H ; otherwise store FF H .

Line#	Address in Hex	Label	Instruction	Opcode in Hex	Remarks
1	0800		LXI H,204FH	21	Get the input N
2	0801			4F
3	0802			20
4	0803		MOV C,M	4E	C = M
5	0804		MVI D, 01H	16	Store index of current element
6	0805			01
7	0806		LDA 204EH	3A	Load the number to be searched.
	0807			4E
	0808			20
10	0809		MOV B,A	47	B = A
11	080A	REPEAT	INX H	23	Go to next address
12	080B		MOV A,M	32	A = M
13	080C		CMP B	B8	A - B
14	080D		JNZ NEXT	C2	Jump to NEXT if A is not equal to B.
	080E			15
	080F			08
15	0810		MOV A,D	7A	A = D
16	0811		STA 204DH	32	Store index of number found
	0812			4D
	0813			20
19	0814		HLT	76	Halt
20	0815	NEXT	MVI A, FFH	3E	A = FFH
	0816			FF
22	0817		STA 204DH	32	Store FF to indicate that number not found yet.
	0818			4D
	0819			20
25	081A		INR D	14	D = D + 1
26	081B		DCR C	0D	C = C - 1
27	081C		JNZ REPEAT	C2	Jump to REPEAT until C = 0
	081D			0A
	081E			08
28	081F		HLT	76	Halt

Simulator with loaded machine code:

Sample input and output ( M[204F] = 05H, M[2050] = 01H, M[2051] = 05H, M[2052] = E0H, M[2053] = 08H, M[2054] = F0H, M[204E] = 05H => M[204D] = 02H):